Office of The Municipal Councillors of Bankura Municipality                        Page-1

Bankura

NOTICE  INVITING  QUOTATION

Memo No:1893/V-I                                                                                                                    Date: 22.11.12

Sealed quotation are invited from the bonafide, resourceful & proven manufacturers as well as the authorized dealers of DI (Ductile Iron) pipes for supply and delivery ( including loading and unloading) of Socket & Spigot Centrifugally Cast (Spun) DI pressure pipes for work under Bankura Municipality.

SPECIFICATION OF DI PIPES & SPECIALS:

ISI marked socket and spigot end centrifugally cast (spun) Ductile Iron Pipe of class K9/K7 conforming to IS:8329/2000 (including rubber gasket) suitable for push on joining with internal cement mortar lining and external protection by zinc coating with finish layer of synthetic resin (blue/black epoxy coating) and DI specials as per IS:9523

DETAILS OF METERIALS:

| S.L No. | Dia (mm) | Class | For site price ( Rs./ Mtr) under ED Exempted Category / With ED paid |
| --- | --- | --- | --- |
| 1 | 100 | K7 |  |
| 2 | 150 | K7 |  |
| 3 | 200 | K7 |  |
| 4 | 250 | K7,K9 |  |
| 5 | 300 | K7,K9 |  |

Qualification required for eligible bidders:

- Manufacture should furnish valid BIS license issued by competent authority of BIS operating to manufacture/ producer DI pipes class K7 & K9 diameter 100 mm to 500 mm as per IS: 8329/ 2000 on the date of submission of Bid.

- Manufacture should furnish satisfactory Performance Certificate for the DI pipe of diameter ranging from 100mm to 500 mm supplied by them for any govt. / ULB water supply project from officer not bellow the rank of Executive Engineer. Failing with their Part I: Technical bid shall be summarily rejected.

- Joint Leak Tightness Test- As per clause 6.3 of is 8329:2000, manufacturers should ensure that the joint  (Socket & Compatible Rubber Gasket) is designed to provide adequate joint performance up to the highest possible pressure, i,e. max. allowable site test pressure (STP) as per Table I of Annexure E of IS: 8329:2000. So efficacy of joint design has to be proved by suitable Type Tests ( proof of design test which is done once) and test results, certified by a Govt. recognized Institution/Inspection agency are to be submitted with the Technical Bid.

- Cement Lining Smoothness Type Test-To ensure desired hydraulic Smoothness of Cement Mortar Lining , the pipe manufacture should submit “C” value type test certificate (proof of design test which is done once ) showing the minimum Hazen William’s “C” value of 140, corroborating the guideline of CPHEEO’S manual water supply and Treatment (Table6.1 page 108). The “C” value type test result certified by a Govt. recognized Institution/Inspection agency to be submitted with Technical Bid. The test sample diameters shall be chosen as per clause 9.2 of IS: 8329:2000.

Page- 2

- Potability Test – Bidders shall ensure that the paint used inside the socket and the part of spigot engaged in the joint assembly, cement mortar lining and rubber gasket which come in contact with potable water, will not have any detrimental effect on the quality of water and should not impart any bad taste or foul odor as per clause no. 8.5 and 14 of IS:8329:2000. Necessary Test Certificate from a recognized Institution /Inspection agency is to be submitted with the Technical Bid . Bidders are  requested to submit all the above documents/undertaking duly notarized in the part –I Technical Bid, failing which the part –II : price Bid will not be considered for opening being the part – I Technical Bid as non responsive one.

- The detailed N.I.Q. documents and other relevant particulars (if any) may be seen by the intending quotationer during  office hours in the office of the Chairperson, Bankura Municipality . The offered rate, if accepted, will be valid for the year 2012-2013  & 2013-14

- If any pipe fails to withstand the pressure as suggested in the quotation paper during execution the same will have to be replaced, as per the quotation specification, by the agency at their own cost without any claim within 7(seven) days (or as suggested by the Chairperson, Bankura Municipality).

- The rate quoted should be inclusive of all costs including transport , loading , unloading , staking at site and all taxes , vat, etc. what so ever .

- The interested quotationer shall have to produce valid I.T, P.T. & VAT clearance certificates , PAN card & other documents.

- Quotation rate must reach in this office by 17.12.2012   at 1 P.M. through by post,courier or E-mail (bankuramunicipality @rediffmail.com.).

- This N.I.Q. may be seen in our website www.bankuramunicipality.org

** Last date & time limit of receiving quotation paper at office of the Bankura Municipality On. 17.12.2012                  at 2 P.M.

** Date & time of opening quotation paper at office of the Bankura Municipality    on: 17.12.2012       at 3 P.M.

Municipal authority reserves the right to accept or reject any or all the quotations without assigning any reason whatsoever .

SD/-

Chairperson

Bankura Municipality

Copy forwarded to:

Memo No. 			Date.

- The District Magistrate, Bankura

- The Sabhadhipati , Bankura Zila Parishad

- The Suprintendent of post office, Bankura

- The Urban Planner, Bankura Municipality for wide publication in the municipal website.

SD/-

Chairperson

Bankura Municipality